## Slide 1: Windows Driver Verification
David Lariviere
COMS E6998 – Formal H/S Verification

## Slide 2: Presentation Outline
Windows Drivers
Microsoft Verification Tools
Operating Systems 101
Examples:
  PortTalk
  SDV’s “Fail_driver1” Example
  Eightball
Conclusions

## Slide 3: Microsoft Windows Drivers
Can be EXTREMELY confusing.
  Many different ways to achieve the same thing.
  Constantly changing
Many different Libraries have been used over time:
  Virtual Device Driver (VxD):
    Windows 3.x, 95, 98, and ME
  Windows NT Driver Model:
    Windows NT
  Windows Driver Model (WDM):
    Introduced in Windows 98 and 2000.
    Must be either a bus, function, or filter driver.
    Must support PnP, Power Management, and WMI.
  Windows Driver Foundation (WDF):
    Windows 2000, XP, Server 2003, and Vista
    Kernel-Mode Driver Framework (KMDF):
      Windows 2000, XP, Server 2003, and Vista
      used to create drivers that conform to WDM
      simplifies common complicated tasks, like PnP and Power Management
    User-mode Driver Framework (UMDF):
      Windows XP and Vista
      Used in cases where running within the kernel not necessary.

## Slide 4: Basic Driver Model
Taken from WDK – “Overview of System Components for Driver Writers”

## Slide 5: Overview of Windows Components
Taken from WDK: “Overview of Windows Components”

## Slide 6: WDM Driver Types
Filter Driver: filters requests between other drivers.
Function Drivers: control individual device
Bus Drivers: Services a bus controller, adapter, or bridge (USB, PCI, etc)
Taken from WDK: “Types of WDM Drivers”

## Slide 7: WDM Types Example – USB Joystick
Taken from WDK: “WDM Driver Layers: An Example”

## Slide 8: I/O Request Packets (IRP)
Drivers Communicate with IRPs.
IRPs are passed through the Driver stack, as multiple drivers process and pass on the driver.
Analogy: TCP/IP, where each Router is a driver.
Taken from WDK: “Example I/O Request – An Overview”

## Slide 9: IRQ Levels (IRQL)
Different driver routine execute at different levels (from lowest to highest priority)
  PASSIVE_LEVEL:
  APC_LEVEL:
  DISPATCH_LEVEL:
  DIRQL:
IRQL indicates which interrupts are turned off, and therefore which functions can be safely called.
Example:
  A routine called @ the DIRQL (highest priority) will have all interrupts turned off, including page fault interrupts.
  Therefore it cannot access any memory that might be paged!
Taken from WDK: “Managing Hardware Priorities”

## Slide 10: Microsoft Verification Tools
It is hopefully now clear that writing drivers can be difficult, let alone writing correct bug-free drivers.
Verification tools to the Rescue!
  PREfast
  Static Driver Verifier
  Driver Verifier

## Slide 11: The following slides are taken from “Static Analysis and Verification of Drivers” WINHEC 2006 by Donn Terry and Vlad Levin of Microsoft. Property of Microsoft. Used explicitly for Academic purposes…. Please don’t sue me 
* Located @ http://www.microsoft.com/whdc/devtools/tools/SDV.mspx

## Slide 12: Static Analysis – How Does It Work?
The tool builds an abstract model of a driver and exhaustively inspects execution along all paths
  The abstract model is simpler: it’s reduced...
  It’s so much simpler that it’s possible to have it inspected (“simulated”) exhaustively
Over-approximation of the driver
  The control part remains the same
    All paths are preserved and treated equally
  The data state is over-approximated
    if argument x is not constrained, assume any value
    if (x>0) guards the point of interest, keep track of boolean (x>0), but not integer value of x: boolean is simpler than integer
      if (x > 0) { IoCompleteRequest (Irp); }

## Slide 13: Static Analysis Not a silver bullet
Does not replace functional testing
Targets violations of a given set of well-defined constraints
Principal limitation
  It doesn’t know about every possible error
  Algorithms are based on source code abstraction and heuristics
    Which results in both false positives and false negatives
It is not a silver bullet…
It is a useful tool

## Slide 14: Our Static Tools For Drivers
PREfast For Drivers (PFD)
  Lightweight and fast (runs in minutes)
  Easy to use early in development – start early
    Use on any code that compiles
  Limited to a procedure scope
  Works on any code, C and C++
  Finds many local violations
Static Driver Verifier (SDV)
  Extremely deep analysis (runs in hours)
  More useful in the later stages of development
    Requires complete driver
    Works over the whole driver
  Limited to WDM and to C (more planned)
  Finds deep bugs

## Slide 15: Driver Tools Relationship
A problem has been detected and Windows has been shut down to prevent
Damage to your computer.
DRIVER_IRQL_NOT_LESS_OR_EQUAL
If this is the first time you've seen this Stop error screen,
restart your computer. If this screen appears again, follow
these steps:
Check to make sure any new hardware or software is properly installed.
If this is a new installation, ask your hardware or software
Manufacturer for any Windows updates you might need.
If problems continue, disable or remove any newly installed hardware
or software. Disable BIOS memory options such as caching or shadowing.
If you need to use Safe Mode to remove or disable components, restart
your computer, press F8 to select Advanced Startup Options, and then
select Safe Mode
Technical information:
*** STOP: 0x00000001 (0x0000000,00000002,0x00000000,0x00000000)
Easy Reproducibility Hard
Depth
Driver
Verifier
Static Driver
Verifier
PREfast for drivers
Hard
Ease Of Use
Complex

## Slide 16: SDV: Quality
Comprehensive path coverage
  Checks all possible paths in a driver
  Checks cross procedure calls
  Checks a driver together with libraries
Finds deep defects that are hard to repro
SDV is not perfect
  Only one driver (not the entire driver stack)
  DDI implementation code is abstracted away
  Might run out of time

## Slide 17
End of copied slides Seriously, don’t sue .

## Slide 18: Operating Systems 101 - Modes
Modern-day CPUs provide support for operating in different modes.
The mode of operation determines what machine instructions and areas of memory can and cannot be accessed.
Two main modes:
  User: regular software
  System (Protected): OS and Drivers

## Slide 19: Operating Systems 101 - Paging
Paging and Virtual Memory:
  Increase size of available memory (beyond physical RAM) to programs by storing parts of the memory space on the HD.
  Memory is broken up into chunks called pages.
  Not all of a program’s pages will necessarily be in memory when the program is running.
  Up to Operating System (Kernel) + Hardware (MMU) to implement and handle.

## Slide 20: OS 101 – Memory Mapped I/O
Memory Mapped I/O: hardware is mapped to memory addresses.
Example: Parallel port
  LPT1: mapped to 0x3bc0x3bf
  Writing to the destination will actually set the pins on the port high or low.
  Reading will provide input from peripherals driving the pins.
Using original PCs (including Win9x), user-mode software could access the memory-locations directly, thus controlling the PPs.
On NT-based versions of Windows (with protected memory) user-mode programs cannot access the memory values directly.
Segway!

## Slide 21: Introducing PortTalk
An Open-source Windows Driver for accessing the parallel port.
Written by Craig Peacock (thank you!)
Allows user mode programs (through the PortTalk driver) to control the PP
http://www.beyondlogic.org/porttalk/porttalk.htm

## Slide 22: Case Study – Verifying PortTalk
PREfast:
  Found 4 Warnings
    The first always appears, stating it is not actually a warning.
    The second was a false-positive.
    The third and fourth were legitimate bugs.
SDV:
  No SDV rules applied. 

## Slide 23: PREfast – False Positive
Virtually every driver has the same initial routine in the DriverEntry function:
NTSTATUS DriverEntry(
IN PDRIVER_OBJECT DriverObject,
IN PUNICODE_STRING RegistryPath
)
{
PDEVICE_OBJECT deviceObject;
NTSTATUS status;
WCHAR NameBuffer[] = L"\\Device\\PortTalk";
WCHAR DOSNameBuffer[] = L"\\DosDevices\\PortTalk";
UNICODE_STRING uniNameString, uniDOSString;
…
…
status = IoCreateDevice(DriverObject,
0,
&uniNameString,
FILE_DEVICE_UNKNOWN,
0,
FALSE,
&deviceObject);
Notice in IoCreateDevice we pass a pointer to deviceObject. This is so that IoCreateDevice can put the object there.
PREfast warned it might be a memory leak.
In other situations, it is a legitimate concern.

## Slide 24: PREfast – Pointer Bugs
Within the PortTalk code are some Debug statements:
KdPrint( ("PORTTALK: Offset = %d, Value = %d\n",Offset,Value) );
Where offset and value are pointers.
PREfast warned that one must not use %d for pointers, since on a 64-bit machine pointers are 64-bits, but %d is explicitly for 32-bit integers.
PREfast even gave the correct solution of using %X (specifically for pointers) instead.

## Slide 25: SDV - failed_driver1
SDV comes with a few example drivers that are inccorect, including failed_driver1.
It contains 6 common mistakes that SDV checks for.
  CancelSpinLock
  IrpProcessingComplete
  IrqlReturn
  LowerDriverReturn
  NullExFreePool
  SpinLock

## Slide 26: SDV - CancelSpinLock
CancelSpinLock rule requires:
  that the driver calls IoAcquireCancelSpinLock before calling IoReleaseCancel
  That the driver calls IoReleaseCancelSpinLock before any subsequent calls to IoAcquireCancelSpinLock
  The driver must not hold any spin locks when the dispatch routine or cancel routine ends.

## Slide 27: SDV - NullExFreePool
NullExFreePool prohibits a driver from calling ExFreePool on a NULL pointer.

## Slide 28: SDV on Custom Driver
As part of project, I am also writing another driver, and verifying it along the way.
PREfast has been (usually) quite helpful.
SDV…. has not.

## Slide 29: DriverEntry Bugs

## Slide 30: DriverEntry Bugs Explained
The previous code segment violated at least three rules (all intentionally):
  SafeStrings
  CancelSpinLock
  NullExFreePool
According to SDV, however:
  SafeStrings does not apply.
  CancelSpinLock passes
  NullExFreePool: fails

## Slide 31: Origin of Previous Test
Originally, I was trying to debug another portion of the code for safe strings, but SDV was reporting the SafeStrings rule did not apply (meaning no unsafe string functions were being used).
Strlen is an unsafe string function.
Fearing SDV wasn’t analyzing the specific function within the code, I moved the test into DriverEntry.
After it still wasn’t applying, I decided to include a rule taken directly from the failed example driver... But it passed!
Fearing SDV still wasn’t actually scanning the code, I added yet another failed example code chunk… it finally failed, meaning SDV was actually processing the code!

## Slide 32: Woes of Driver Development
My machine after falling victim to a paging bug which neither PREfast nor SDV found.

## Slide 33: Conclusions
PREfast is great.
  Extremely quickly finds many common mistakes.
  Sometimes reports false positives on some very common cases.
  Offers (sometimes unjustified) peace of mind while writing drivers.
SDV…
  Supposedly very good at finding extremely complex bugs with extremely difficult paths.
  Showed difficulty finding some very simple bugs.
  Might be buggy…